## Slide 1
1. Extract requirements
Req. Spec.
Requirement list, CSV
<Req. Label>, <Description>
<Req. Label>, <Description>
……….
2. Implement Testcase
4. Run specification coverage (run_spec_cov.py)
Specification Coverage, CSV
Three files are generated: (see ch. 10.2) - Compliance for Reqs. vs single testcase
- Compliance for Reqs. vs multiple testcases - Status for Reqs. in each testcase
Requirement list, CSV
UART_REQ_1, Baudrate 9k6
UART_REQ_2, Baudrate 19k2
UART_REQ_3, Odd parity
UART_REQ_4, Active low reset
Ext. Input Development flow Files examples, Generic File Examples Testcase sequencer example (VHDL)
Inside the testcase sequencer:
-- Assume one simple testcase: t_basic
Initialize_req_cov(<testcase-name>, <req_list-file>, <coverage_file>);
-- Test sequence to verify UART_REQ_1 and UART_REQ_3 here actually at the same time
tick_off_req_cov("UART_REQ_1"); tick_off_req_cov("UART_REQ_3");
-- Test sequence to verify UART_REQ_2 tick_off__req_cov("UART_REQ_2");
-- etc
finalize_req_cov(VOID);
Specification coverage, CSV
(Excerpts from 'Reqs vs single testcase) UART_REQ_1, tc_basic, COMPLIANT UART_REQ_2, tc_basic, COMPLIANT UART_REQ_3, tc_basic, NON_COMPLIANT (See ch. 10.2 for details)
RL
SC
T
RL
SC
T1
T2
T3
3. Run Testcase
TC
Partial Coverage, CSV
UART_REQ_1, tc_basic, PASS
UART_REQ_2, tc_basic, FAIL
UART_REQ_3, tc_basic, PASS
UART_REQ_4, tc_basic, PASS
PC
Requirement list, CSV
<Req. Label>, <Description> [, <Testcase-name>, <Testcase-name>, <Testcase-name>, …]
<Req. Label>, <Description> [, <Testcase-name>, <Testcase-name>, <Testcase-name>, …]
……….
Requirement list, CSV
UART_REQ_1, Baudrate 9k6 , tc_basic
UART_REQ_2, Baudrate 19k2 , tc_19k2
UART_REQ_3, Odd parity , tc_basic, tc_19k2
UART_REQ_4, Active low reset, tc_reset, tc_basic, tc_19k2
RL
RL
Requirement list, CSV
UART_REQ_1, Baudrate 9k6 , tc_basic
UART_REQ_2, Baudrate 19k2 , tc_19k2
UART_REQ_3, Odd parity , tc_basic
UART_REQ_3, Odd parity , tc_19k2
UART_REQ_4, Active low reset, tc_reset, tc_basic, tc_19k2
RL
Partial Coverage, CSV
<Req. Label>, <Testcase>, <test_status>
<Req. Label>, <Testcase>, <test_status>
……….
PC
Requirement list, CSV
<Req. Label>, <Description>[, <Testcase-name>]
<Req. Label>, <Description>[, <Testcase-name>]
……….
Requirement list, CSV
UART_REQ_1, Baudrate 9k6 , tc_basic
UART_REQ_2, Baudrate 19k2 , tc_19k2
UART_REQ_3, Odd parity , tc_basic
UART_REQ_4, Active low reset, tc_reset,
RL
RL

## Slide 2
Requirement list, CSV
UART_REQ_1, Baudrate 9k6 , tc_basic
UART_REQ_2, Baudrate 19k2 , tc_19k2
UART_REQ_3, Odd parity , tc_basic
UART_REQ_4, Active low reset, tc_reset
RL
From the UART IP
Requirement list, CSV
UART_REQ_A, Baudrate 9k6 and 19k2
UART_REQ_B, Odd parity
RL
From the PROJECT requirements
Requirement map file, CSV
UART_REQ_A, UART_REQ_1, UART_REQ_2
UART_REQ_B, UART_REQ_3
RM

## Slide 3
From the UART IP
Partial coverage 1
Testcase 1
Testcase 1
Testcase 1
Partial coverage N
(CSV)
Testcase 1
Testcase 1
Testcase 1
Testcase 1
Testcase N
(VHDL)
Specification coverage
files
(CSV)
Post processing
(Python)
Requirement list
(CSV)
Partial coverage 1
Testcase 1
Testcase 1
Testcase 1
Partial coverage N
(CSV)
Testcase 1
Testcase 1
Testcase 1
Testcase 1
Testcase N
(VHDL)
Specification coverage
files
(CSV)
Post processing
(Python)
Requirement list
(CSV)