## Slide 1
1. Extract requirements
Req. Spec.
Requirement list, CSV
<Req. Label>, <Description>
<Req. Label>, <Description>
……….
2. Implement Testcase
4. Run specification coverage (run_spec_cov.py)
Specification Coverage, CSV
<Req. Label>, <Compliancy>
<Req. Label>, <Compliancy>
……….
Requirement list, CSV
UART_REQ_1, Baudrate 9k6
UART_REQ_2, Baudrate 19k2
UART_REQ_3, Odd parity
UART_REQ_4, Active low reset
Ext. Input Development flow Files examples, Generic File Examples Testcase sequencer example (VHDL)
Inside the testcase sequencer:
Initialize_req_cov(<testcase-name>, <req_list-file>, <coverage_file>);
-- Test sequence to verify UART_REQ_1 and UART_REQ_2
log_req_cov(UART_REQ_1); log_req_cov(UART_REQ_2);
-- Test sequence to verify UART_REQ_3 log_req_cov(UART_REQ_3);
-- etc
finalize_req_cov(VOID);
Specification coverage, CSV
UART_REQ_1, COMPLIANT
UART_REQ_2, NON COMPLIANT
UART_REQ_3, COMPLIANT
UART_REQ_4, COMPLIANT
RL
SC
T
RL
CS
T1
T2
T3
3. Run Testcase
TC
Testcase Coverage, CSV
UART_REQ_1, T_9k6, PASS
UART_REQ_2, T_19k2, FAIL
UART_REQ_3, T_9k6, PASS
UART_REQ_4, T_reset, PASS
TC
Requirement list, CSV
<Req. Label>, <Description>, <Testcase-name>
<Req. Label>, <Description>, <Testcase-name>
……….
Requirement list, CSV
UART_REQ_1, Baudrate 9k6 , T_9k6
UART_REQ_2, Baudrate 19k2 , T_19k2
UART_REQ_3, Odd parity , T_9k6
UART_REQ_4, Active low reset, T_reset,
RL
RL
Requirement list, CSV
<Req. Label>, <Description>, <Testcase-name> [, <Testcase-name>, <Testcase-name>, …]
<Req. Label>, <Description>, <Testcase-name> [, <Testcase-name>, <Testcase-name>, …]
……….
Requirement list, CSV
UART_REQ_1, Baudrate 9k6 , T_9k6
UART_REQ_2, Baudrate 19k2 , T_19k2
UART_REQ_3, Odd parity , T_9k6, T_19k2
UART_REQ_4, Active low reset, T_reset, T_9k6, T_19k2
RL
RL
Requirement list, CSV
UART_REQ_1, Baudrate 9k6 , T_9k6
UART_REQ_2, Baudrate 19k2 , T_19k2
UART_REQ_3, Odd parity , T_9k6
UART_REQ_3, Odd parity , T_19k2
UART_REQ_4, Active low reset, T_reset, T_9k6, T_19k2
RL
Testcase Coverage, CSV
<Req. Label>, <Testcase>, <test_status>
<Req. Label>, <Testcase>, <test_status>
……….
TC

## Slide 2
Requirement list, CSV
UART_REQ_1, Baudrate 9k6 , T_9k6
UART_REQ_2, Baudrate 19k2 , T_19k2
UART_REQ_3, Odd parity , T_9k6
UART_REQ_4, Active low reset, T_reset,
RL
From the UART IP
Requirement list, CSV
UART_REQ_A, Baudrate 9k6 and 19k2
UART_REQ_B, Odd parity
RL
From the PROJECT requirements
Requirement map file, CSV
UART_REQ_A, UART_REQ_1, UART_REQ_2
UART_REQ_B, UART_REQ_3
RM